## Slide 1
CTUIR ~ Tucannon Basin Fish Habitat Enhancement Project
Project Area 27/28.1
Photo of PA-27/28.1, 2/2020
Kris Fischer, Tucannon Basin Project Leader
Amanda Jones & Allen Dysart, Wolf Water Resources
Notes: Wolf logo

## Slide 2
Presentation overview:
Introduction to PA 27/28.1 in the Tucannon
River Vision and First Foods
Tucannon – Impaired Processes and Limiting Factors
Tucannon – Channel straightening over time
PA-27/28 – Restoration Approach
PA-27/28.1 Design Component and Permitting
USCOE HEC-RAS Modeling
Additional Phases of this project
Some good news, we saw fish this summer
King Grade Road, 2/2020
PA 27/28.1
Notes: Todays presentation includes:

## Slide 3
CTUIR - River and Upland Vision
RV - Requires a river that is dynamic, and shaped not only by physical and biological processes, but the interactions and interconnections between those processes
CTUIR Seasonal Round
Hydrology
Geomorphology
Connectivity
Riparian Vegetation
Aquatic Biota
Notes: What is the tribal approach to solving problems in the Tucannon?
The First Foods approach requires us to get our heads out of the channel and look for restoration opportunities on the floodplain and uplands. The holistic approach is necessary to provide for all first foods within the seasonal round.
Rebuilding ecological resilience within these river systems, means putting the missing ecological pieces (think River Vision touchstones) back in place like puzzle pieces, allowing these systems to once again be resistant to disturbance so the existing channel processes and forms are recognizable to the native species that depend on them. (Fuller et al. 2019, Tullos et al. 2021)
Resilient river systems not only provide good places for fish and wildlife, but also protect communities from flooding, droughts and wildfire.
The aquatic biota touchstone functions as a response variable to the other four River Vision touchstones.
The Seasonal Round displays the first food resources that the tribes subsisted on each month of the year.

## Slide 4
Geomorphology
Connectivity
Riparian Vegetation
Aquatic Biota
Tucannon spring Chinook – Impaired Processes
Reduced in-channel wood
Modified sediment delivery and transport
Reduced floodplain connectivity and function
Reduced riparian condition and function
Table 6-2 (Pg 50) in the 2020 Plan by AnchorQEA
These impaired processes have negative impacts on spring Chinook and others.

## Slide 5
Geomorphology
Connectivity
Riparian Vegetation
Aquatic Biota
Tucannon spring Chinook – Limiting Factors
Low diversity of in-channel habitats
Lack of deep pools for holding and rearing
Reduced quality of spawning gravel
Low diversity of off-channel habitats
Lack of high-flow refuge
Reduced groundwater recharge and summer discharge
Limited hiding cover
Lack of shade causing high water temperatures
Table 6-2 (Pg 50) in the 2020 Plan by AnchorQEA
Together these limiting factors have negative impacts on spring Chinook and others.

## Slide 6
Channel Lengths
1937 = 8,240 ft
1978 = 7,105 ft
2020 = 7,025 ft
Channel length changes from 1937 to 2020 @PA-27/28.1
Hecht, 1982
2020
Notes: Now I want to focus on our work in PA-27/28.
I’ve included the old channel traces from Barry Hecht in 1982 as a visual reference to the changes in many reaches of the Tucannon.
Notice the channel length and pattern changes from 1937 in blue to 1978 in red.
The 1937 channel length was 8,240 ft and by 1978 was reduced to 7,105 ft.

## Slide 7
PA 27/28.1 Restoration Goals
Increase Floodplain connectivity
Maximize channel complexity
Deep pools, side channels, and gravel bars
Dissipate stream power

## Slide 8
PA 27/28.1 Design
Notes: Add plans PDF

## Slide 9
Environmental Review
Design and BPA HIP Review
Cultural Review
30% Design
BPA HIP Review
Final Plans
BPA HIP Review
60% Design and Model Development
BPA HIP Review and Form to NMFS & USFWS
Cultural Survey
JARPA based on 60% Design and Description
Regulatory Agency Review - Only complete once the Corps has documentation of HIP, Cultural, and Environmental Review from BPA
Wetland Assessment
Implementation!
Design Process and Permitting
Notes: Design process

## Slide 10: Design Components
Floodplain grading: removal of artificially high areas (berms and roads), lowering of the disconnected floodplain terrace. Low areas such as wetlands are avoided with floodplain excavations
Channel Filling: filling of the channel, raising the bed elevation with material excavated from high floodplain areas, reversing incised areas
Increase Floodplain Roughness: Placement of loose logs, tipping of existing trees, beaver dam analogs, and other roughness elements
Common features: Leave pools, leave islands, emulated landslides, partially buried WHS, preserving relic channels

## Slide 11
Notes: Existing – single threaded channel, very little wood
Prop – multithreaded channel with side channels and wood habitat structures in the channel and across the floodplain

## Slide 12
Wood Habitat Structures

## Slide 13
Post-project September 2021
911 LWD (>6m long & 0.3m dia.)
81 pools (#)
5,730 (m2) pool area
2,231 m perennial side channel
2410 m of high flow channels
1.65 km main channel length
Pre-project July 2020
107 LWD (>6m long & 0.3m dia.)
43 pools (#)
1,956 (m2) pool area
474 m perennial side channel
669 m of high flow channels
1.51 km main channel length

## Slide 14
Pre-Project 2020
Notes: Change photo to stream

## Slide 15
Post-Project 2021
Notes: Change photo to stream

## Slide 16
HEC-RAS 2D Hydraulic Modeling
Hydraulic Engineering Center – River Analysis System (HEC-RAS)
Publicly available and produced by the US Army Corps of Engineers
HEC-RAS is used on flood-study and river engineering projects world-wide.
This software allows the user to perform one-dimensional steady flow, one and two-dimensional unsteady flow calculations, sediment transport/mobile bed computations, and water temperature/water quality modeling.
Hydraulic Model Inputs:
Topographic/bathymetric surface data (e.g. LIDAR)
Flow input time-series
Landcover (Manning’s n)
Structure Geometry (e.g. bridges, culverts, etc.)
2D Mesh
Notes: Modeling intro

## Slide 17
Post-project 25-year velocities
Kings Grade Rd
Modeled velocities during a 25-year event.

## Slide 18
Post-project increase in base-flow wetted area.

## Slide 19
Decreased velocities in the mainstem are a result of additional flow depth on the floodplain, and within connected side channels.
Mainstem velocities decreased by ~1-3 ft/s
Post-project change in 2-year velocities
Change in Mainstem Velocity

## Slide 20
Receding flood waters during the February 2020 flood at the site of the Tucannon River 27-28 Restoration Project. Approximate flow of 1,200 cfs.
King Grade Road
Notes: Combine with previous

## Slide 21
Existing conveyance during a 25-year event.
Bridge
Q25 = 2212 cfs
36” CMP Culvert
Q25 = 22 cfs
12” CMP Culverts (2)
Q25 = 6 cfs
S. Riparian
Q25 = 295 cfs
N. Riparian
Q25 = 521 cfs
Field
Q25 = 505 cfs
Total Structural Conveyance = 2240 cfs
Total Floodplain Conveyance = 1321 cfs
Kings Grade Rd.

## Slide 22
Post flood (2020) photos showing only minor damage to the King’s Grade Road surface within the project site.
Notes: Extend to full slide and clean up pictures

## Slide 23
Bridge failure and road washout along a confined reach of the Tucannon River by Watson Lake following the February 2020 flood.
Notes: Extend to full slide

## Slide 24
Tucannon PA-27/28.1
Phase 1
Phase 2
Phase 3
Phase 4
Notes: Currently we are working on floodplain connection project on private lands in PA-27/28.1 near King Grade. The originally plan for Phase 1 included all the in-channel work, but because of delays caused by covid 19, Phase 1 work was cut in half. The first part of Phase 1 was completed in the summer of 2020 – with work starting in the middle of the project area. The in-channel work included 350 large trees both in channel and on the floodplain to help reduce velocities and increase depth thru this site. An existing ditch was filled, and side channels were excavated to help reconnect the floodplain.
Phase 2 completed this summer (2021) – completes the in-channel work, occurring both upstream and downstream of the 1st Phase. An additional 350 large trees were placed in the channel and on the floodplain. There were 3 large channel spanning log jams to help dissipate velocities at the bottom end of the project area, before the river leaves the landowner’s property.
Phase 3 – Plans for 2022, include Irrigation efficiencies, water rights transfers and a 13 acre floodplain easement. Before starting restoration in the floodplain, we are working with our landowners and the tribe’s water transactions program to plan the modifications to the irrigation infrastructure on the property. To help offset the costs of the irrigation efficiencies, we plan to compete a floodplain easement and transfer water back instream.
Phase 4- is the 13 acres of floodplain reconnection. This project is still in the early planning phase, but the design is expected once phase 3 is complete. We anticipate having one full year of irrigation efficiency to make sure the farm is operating properly, before we start construction on the floodplain connectivity.
The floodplain acres are currently the most productive part of the property, so we want to make sure the newly installed irrigation in the upland fields help offset any losses caused by the conversion of the lower field back to floodplain. As you can tell by the photo, plans need to be made to revegetate the lower field, before water is turned out there on an annual basis so we don’t have any unintended short-term temperatures increases during the summer.

## Slide 25: Side Channels to improve Floodplain Connectivity
Notes: When building side channels we are mindful not to further incise the channel network, or lock the system to its existing bed configuration. We are looking for channel aggradation and are expecting the river to do most of the work. Often we start the side channels, with pilot cuts and let the river do the rest of the work.

## Slide 26: Gravel Bars for in Channel Complexity
Notes: Complexity is very important for salmon at all life stages, this condition vastly increases the number of available habitat units over the single thread channel.

## Slide 27: Large wood to increase Channel and Floodplain Roughness
Notes: Large wood in the channel and on the floodplain reduce velocities, causing channel aggradation while providing velocity refuge for salmon during all life stages.

## Slide 28: Gravel Deposition for Spawning Beds and Hyporheic Flow
Notes: Roughness causes gravel deposition, which is important for both redd development and for hyporheic flows.
Hyporheic flows help to replenish the ground water aquifer, think of it as re-wetting the sponge, this stored water helps decrease temperatures in the summer, but also helps increases temperature in the winter time to reduce the formation of anchor ice.
The ground water aquifer helps to extend flows further into the summer, which is beneficial to fish and wildlife, and Tucannon water rights users.

## Slide 29
PA-27/28.1 Fish Salvage Operations in 2021
The Good News!
There are fish below Marengo in the summer time!
We carefully moved:
52 - Spring Chinook
504 - Steelhead

## Slide 30: Thanks
Floodplain connectivity on PA 18 completed in 2017